## Slide 1: An algorithm for the elimination of all first order internal multiples from all reflectors in a 1D medium: theory and TESTS including bandwidth and noise
Yanglei Zou

## Slide 2
Internal multiple removal

## Slide 3
Internal multiple removal
Internal multiple attenuation algorithm
Araújo et al(1994)，Weglein et al. (1997)
Notes: The ISS first order internal multiples attenuator provides the exact time and approximate amplitude of all first order internal multiples that have a single downward reflection at any reflector.

## Slide 4: Algorithm & Adaptive
Case 2
predicted
multiple
Case 1
predicted
multiple
data
data
Internal multiple attenuation
+ adaptive subtraction
Solution
Solution
Internal multiple elimination
Notes: On shore data, and off shore data

## Slide 5
Internal multiple removal
Spurious events removal
Ma et al(2012),Liang et al(2012)
Predicting correct amplitude
Internal multiple attenuation algorithm
Araújo et al(1994)，Weglein et al. (1997)

## Slide 6
Internal multiple removal
Spurious events removal
Ma et al(2012),Liang et al(2012)
Predicting correct amplitude
Early ideas
Ramírez(2005)
Internal multiple attenuation algorithm
Araújo et al(1994)，Weglein et al. (1997)

## Slide 7
Internal multiple removal
Spurious events removal
Ma et al(2012),Liang et al(2012)
Predicting correct amplitude
Early ideas
Ramírez(2005)
Internal multiple attenuation algorithm
Araújo et al(1994)，Weglein et al. (1997)
Elimination first order internal multiples generated at the shallowest reflector
(1D normal incidence)
Herrera(2012)

## Slide 8
Internal multiple removal
Spurious events removal
Ma et al(2012),Liang et al(2012)
Predicting correct amplitude
Early ideas
Ramírez(2005)
Elimination first order internal multiples generated at the shallowest reflector
(1D normal incidence)
Herrera(2012)
An algorithm to eliminate all first order internal multiples from all reflectors under 1D normal incidence
(This presentation)
Internal multiple attenuation algorithm
Araújo et al(1994)，Weglein et al. (1997)
Notes: This algorithm benefits from the previous work of Welberth Herrera. And it is a generalization of the work.

## Slide 9
Numerical Tests
Conclusion
The structure of this presentation
Amplitude issue
This new elimination algorithm
Attenuation factor
Internal multiple attenuation algorithm
Araújo et al(1994)，Weglein et al. (1997)

## Slide 10
Numerical Tests
Conclusion
The structure of this presentation
Amplitude issue
This new elimination algorithm
Attenuation factor
Internal multiple attenuation algorithm
Araújo et al(1994)，Weglein et al. (1997)

## Slide 11
The 1D normal incidence version of the internal multiple attenuation algorithm is presented as follows:

## Slide 12
AF1= T01T10
Notes: To improve the amplitude, we begin by identifying the difference between the amplitude of the attenuator and the actual internal multiple for the simplest 2 layered case and then we will discuss the the more general case of n reflectors
…
In this case of two reflector, it is relatively easy to see where the fix resides in terms of the data, and that fix for too much T01,T10 come from the b1(z) combination from the inner integral.

## Slide 13
AF1= T01T10
AF2= (T01T10)2T12T21
Notes: Now let us look at a more complex example.
the analysis is much more complicated and the difference is depend on the transmission coefficients down to and including the shallowest downward reflection.
And moving an attenuator into an eliminator needs to correct for a sequence of transmission coefficient at and above the shallowest reflector corresponding to a specific internal multiple.

## Slide 14
A generalization of the attenuation factor(AF) for first order internal multiples(1D normal incidence) is given by the following:
(using transmission coefficients)
(using reflection coefficients)

## Slide 15
Numerical Tests
Conclusion
The structure of this presentation
Amplitude issue
This new elimination algorithm
Attenuation factor
Internal multiple attenuation algorithm
Araújo et al(1994)，Weglein et al. (1997)

## Slide 16
The idea: Modify the term in the second integral to remove the attenuation factor without needing to determine subsurface properties but directly in terms of data.
Notes: 5,Clearer explanation of choosing the middle integral.

## Slide 17
AF2= (T01T10)2T12T21
The idea: Modify the term in the second integral to remove the attenuation factor without needing to determine subsurface properties but directly in terms of data.
Notes: 5,Clearer explanation of choosing the middle integral.
Moving an attenuator into an eliminator needs to correct for a sequence of transmission coefficient at and above the shallowest reflector corresponding to a specific internal multiple.
This procedure is complicated……..

## Slide 18
b1(z)
AF
F[b1(z)]
T
all R
all R’
b1(z)
Notes: T needs to be removed

## Slide 19
b1(z)
AF
F[b1(z)]
T
all R
all R’
b1(z)
Very complex

## Slide 20
b1(z)
AF
F[b1(z)]
T
all R
all R’
b1(z)
Very complex

## Slide 21
partial R’
partial R
b1(z)
g(z)
b1(z)
b1(z)
AF
F[b1(z)]
T
all R
g(z) is a new function defined with R as coefficients.
Notes: b1(z)and g(z) both consider only primaries as input.

## Slide 22
partial R’
partial R
b1(z)
g(z)
b1(z)
b1(z)
AF
F[b1(z)]
T
all R
g(z) is a new function defined with R as coefficients.
b’1(z)=b1(z)+b3IM(z)
Notes: b1(z)and g(z) both consider only primaries as input.

## Slide 23
partial R’
partial R
b’1(z)
g(z)
b’1(z)
b’1(z)
AF
F[b1(z)]
T
all R
g(z) is a new function defined with R as coefficients.
b’1(z)=b1(z)+b3IM(z)
Notes: b1(z)and g(z) both consider only primaries as input.

## Slide 24
g(z) is a new function defined with R as coefficients.
b1(z)
partial R’
partial R
b1(z)
g(z)
b1(z)
b1(z)
AF
F[b1(z)]
F[b1(z)]
T
all R

## Slide 25
b1(z)
partial R’
partial R
b1(z)
g(z)
b1(z)
b1(z)
AF
F[b1(z)]
F[b1(z)]
T
all R

## Slide 26
Numerical Tests
Conclusion
The structure of this presentation
Amplitude issue
This new elimination algorithm
Attenuation factor
Internal multiple attenuation algorithm
Araújo et al(1994)，Weglein et al. (1997)

## Slide 27
In this section we test 3 different equations under 1D normal incidence:
(1) Internal multiple attenuation algorithm
(2) First approximation of the elimination algorithm
(3) Second approximation of the elimination algorithm
(1)
(2)
(3)

## Slide 28
500m
1700m
2700m
5700m
Model
V=1500m/s ρ=1.0g/cm3
V=1700m/s ρ=1.8g/cm3
V=1700m/s ρ=1.0g/cm3
V=3500m/s ρ=4.0g/cm3
V=5000m/s ρ=4.0g/cm3

## Slide 29
Test for perfect data.
Test for band limited data.
Test for data with white noise.
Initial Tests

## Slide 30
Test for perfect data.
Test for band limited data.
Test for data with white noise.
Initial Tests

## Slide 31
The input data(1D normal incidence)

## Slide 32
The input data(1D normal incidence)

## Slide 33
P3
IM212
IM213 and IM312
IM323
P3
IM212
IM213
IM312
IM323
1
2
3
Internal multiple attenuation algorithm

## Slide 34
P3
IM212
IM213
IM312
IM323
1
2
3
First approximation of the elimination algorithm
P3
IM212
IM213 and IM312
IM323

## Slide 35
P3
IM212
IM213
IM312
IM323
1
2
3
Second approximation of the elimination algorithm
P3
IM212
IM213 and IM312
IM323

## Slide 36
Test for perfect data.
Test for band limited data. (10-45Hz)
Test for data with white noise.
Initial Tests

## Slide 37
P3
IM212
IM213 and IM312
IM323
P3
IM212
IM213
IM312
IM323
1
2
3
Internal multiple attenuation algorithm

## Slide 38
P3
IM212
IM213
IM312
IM323
1
2
3
First approximation of the elimination algorithm
P3
IM212
IM213 and IM312
IM323

## Slide 39
P3
IM212
IM213
IM312
IM323
1
2
3
Second approximation of the elimination algorithm
P3
IM212
IM213 and IM312
IM323

## Slide 40
Test for perfect data.
Test for band limited data.
Test for data with white noise.
The energy of noise is 2% of the energy of data.
Initial Tests

## Slide 41
P3
IM212
IM213 and IM312
IM323
P3
IM212
IM213
IM312
IM323
1
2
3
Internal multiple attenuation algorithm

## Slide 42
P3
IM212
IM213
IM312
IM323
1
2
3
First approximation of the elimination algorithm
P3
IM212
IM213 and IM312
IM323

## Slide 43
P3
IM212
IM213
IM312
IM323
1
2
3
Second approximation of the elimination algorithm
P3
IM212
IM213 and IM312
IM323

## Slide 44: Conclusion
In this presentation, a new algorithm is given to eliminate all first order internal multiples under 1D normal incidence directly in terms of data without determining the earth. And this algorithm remains useful with bandwidth and noise.
This algorithm is a part of a project in M-OSRP which is aimed at predicting correct amplitude and time of all internal multiples. This algorithm is a step within seeking this purpose.
There are many cases require new capability for internal multiples removal when primaries and internal multiples interfere with each other in both on-shore and off-shore data. In these cases, the internal multiple elimination project will be particularly relevant and provide value.