## Slide 1
ISS internal multiple attenuation on Encana data set
May 27, 2014
Austin, Texas
Qiang Fu* and Arthur B. Weglein
Notes: 1
1

## Slide 2: The key points
We tested ISS internal multiple attenuation algorithm on Encana data set.
Besides the prerequisites, the ISS algorithm for the surface and internal multiple attenuation requires reasonable data collection in terms of sampling and offset as well
Higher order internal multiple attenuator may be required to better remove higher order internal multiple energy

## Slide 3: Outline
Background
The Encana dataset
The algorithm we choose
Results and discussion
Conclusion

## Slide 4: Outline
Background
The Encana dataset
The algorithm we choose
Results and discussion
Conclusion

## Slide 5: Seismic processing chain
Seismic data processing tasks
Preprocessing
De-multiple
Depth Imaging
Inversion

## Slide 6: Seismic processing chain
Seismic data processing tasks
Preprocessing
De-multiple
Depth Imaging
Inversion
Surface multiple
Internal multiple

## Slide 7: Seismic processing chain
Seismic data processing tasks
Preprocessing
De-multiple
Depth Imaging
Inversion
Surface multiple
Internal multiple

## Slide 8: Seismic processing chain
Seismic data processing tasks
Preprocessing
De-multiple
Depth Imaging
Inversion
Surface multiple
Internal multiple
ISS internal multiple attenuation / elimination

## Slide 9: The ISS internal-multiple attenuation
Advantages of ISS internal-multiple attenuation
Not requirement for subsurface information
Can predict exact time and approximate amplitude
Can predict internal multiples at all depths at once

## Slide 10: The ISS internal-multiple attenuation
Prerequisites for the ISS algorithm to be effective
Reference wave removal
Source wavelet removal
Source and receiver de-ghosting
Free surface multiple removal

## Slide 11: ISS internal multiple attenuation
An intuitive explanation of ISS internal multiple attenuation

## Slide 12: The ISS first-order attenuation
The 2D first-order ISS internal multiple attenuation

## Slide 13: Previous efforts to apply ISS multiple attenuation on field data
Mason et al. 1999 were the first to apply the ISS internal-multiple attenuation on streamer marine data
Matson (1997) and Weglein et al. (1997) extended the ISS method to free-surface and internal multiple on ocean-bottom and land data
Fu et al. (2010) applied ISS internal-multiple attenuation on Arabian Peninsula land field data.
Terenghi (2011) showed ISS internal-multiple attenuation on land data

## Slide 14: Outline
Background
The Encana dataset
The algorithm we choose
Results and discussion
Conclusion

## Slide 15: The Encana data set – stack section

## Slide 16: Geological background
I am not a geologist, so I can not tell you the whole geological background…
There is a coal layer in vicinity of 1 second.
There should be reefs in this area below the coal layer (by well-log of this area)
The reefs is invisible on the data, the reason should be the strong internal-multiple interference caused by the coal layer.
Our goal is to make the reefs to be visible clearly by remove the internal-multiple interference.

## Slide 17: Acquisition parameters
The data set is acquired in mid of 1990s
It is a 2D CMP survey line which consists of 146 CMP stations.
The data set include traces of 4 different azimuths.
The offset interval is 62.5m, and each CMP gather has 32 traces (for single azimuth).
The time sample interval is 0.002s, and there are 1001 time samples per trace.

## Slide 18: The acquisition geometry
Source
Receiver

## Slide 19: One CMP gather - one azimuth
Source
Receiver

## Slide 20: One CMP gather - one azimuth
Source
Receiver
32 receivers
32 sources
CMP point

## Slide 21: One CMP gather - one azimuth
CMP point
receivers
sources
……
……

## Slide 22: One CMP gather - one azimuth
Source
Receiver

## Slide 23: Four CMP gathers for one CMP station - four azimuths
Source
Receiver

## Slide 24: The acquisition geometry
Source
Receiver

## Slide 25: Outline
Background
The Encana dataset
The algorithm we choose
Results and discussion
Conclusion

## Slide 26: Decision to make: 2D vs. 1.5D
The data is a 2D survey line (although there are 4 different azimuths)
However it is only 32 traces per CMP gathers
If we would like to perform 2D ISS internal-multiple attenuation, we would need a large amount of extrapolations to obtain full 2D data coverage from low-fold data that we have.
In addition, we found the subsurface geological structures here is fairly flat.
Thus we choose 1.5D ISS internal-multiple attenuation algorithm.

## Slide 27: The 2D ISS first-order internal multiple attenuation
The 2D first-order ISS internal multiple attenuation

## Slide 28: The 1.5D ISS first-order internal multiple attenuation
1.5D = a 2D source and a 1D earth
The medium consists of horizontal flat-layer reflectors
Under this assumption, and from the symmetry
After the integral over k1 and k2 , we get The 1.5D first-order ISS internal multiple attenuator
My colleague Xinlu Lin will explain more about this topic in her tomorrow presentation

## Slide 29: The 1.5D ISS first-order attenuation
The 1.5D first-order ISS internal multiple attenuation

## Slide 30: The code I used
I used a revised version of ISS internal multiple attenuation code based on Paolo Terenghi’s 1.5D ISS internal prediction code
The Paolo Terenghi’s 1.5D ISS internal prediction code (released in 2012) can be found on M-OSRP website

## Slide 32: Outline
Background
The Encana dataset
The algorithm we choose
Results and discussion
Conclusion

## Slide 33: Stack section of input data

## Slide 34: Stack section of output

## Slide 35: The difference

## Slide 36: Three gathers of input data

## Slide 37: Predicted internal multiple

## Slide 38: Reasons for the not entirely effective
The data set has limited fold per gather (32 trace per DMP gather)
The amplitude in near offset traces is low
There are ambient noise, bad traces (common issues for land data)
There may be a lot of higher order internal multiple energy, the first-order internal multiple attenuator we used may be not sufficient

## Slide 39: Reasons for the not entirely effective

## Slide 40: Conclusions
The earlier Saudi Aramco on-shore ISS internal multiple test (Fu et al 2010) had reasonable multiple offset aperture and produced a successful result. The Encana data set tested in this paper was of an earlier vintage, and had a much smaller maximum offset, and produced a less successful result. Current typical acquisition for marine and on-shore exploration is adequate for ISS internal multiple attenuation effectiveness.
The ISS algorithm for the surface and internal multiple attenuation require reasonable data collection in terms of sampling and offset
Higher order internal multiple attenuator may be required to better remove higher order internal multiple energy

## Slide 41: Acknowledgment
David Mackidd, David Bonar and Encana
Paolo Terenghi
Bill Goodway
All M-OSRP sponsors

## Slide 42: M-OSRP Sponsors

## Slide 43: Thank you