## Slide 1: An internal-multiple elimination algorithm for all first-order internal multiples for a 1D earth
Yanglei Zou* and Arthur B. Weglein

## Slide 2
ISS internal multiple attenuation algorithm
It is the only method that can predict all internal multiples at once with accurate time and approximate amplitude without requiring any subsurface information.
It is model type independent. It is effective for internal multiple removal in acoustic, elastic, absorptive medium et al.
All these huge benefits and advantages make the ISS internal multiple attenuation algorithm standalone and the most capable algorithm today for internal multiple removal.

## Slide 3
Why do we need an internal multiple elimination algorithm?

## Slide 4
1: primaries and internal multiples
are isolated
Solution: ISS Internal-multiple attenuation
+ adaptive subtraction
Why do we need an internal multiple elimination algorithm?
primary
internal multiple

## Slide 5
1: primaries and internal multiples
are isolated
Solution: ISS Internal-multiple attenuation
+ adaptive subtraction
Why do we need an internal multiple elimination algorithm?
primary
internal multiple

## Slide 6
2: primaries and internal multiples
are proximal or interfering
1: primaries and internal multiples
are isolated
Solution: ISS Internal-multiple attenuation
+ adaptive subtraction
Solution: Three-pronged strategy
(including internal-multiple elimination)
Why do we need an internal multiple elimination algorithm?
primary
internal multiple
internal multiple
internal multiple
primary

## Slide 7
2: primaries and internal multiples
are proximal or interfering
1: primaries and internal multiples
are isolated
Solution: ISS Internal-multiple attenuation
+ adaptive subtraction
Solution: Three-pronged strategy
(including internal-multiple elimination)
Why do we need an internal multiple elimination algorithm?
primary
internal multiple
internal multiple
internal multiple
primary

## Slide 8
A three-pronged strategy to address the challenges
  Pre-requisites for on-shore application (Jing Wu, 4:00 PT)
  Stronger ISS internal-multiple-removal algorithm
    within the algorithm
      incorporate dimension of the source (Xinglu Lin, 1:30 PT)
      incorporate radiation pattern of the source (Jinlong Yang, 1:55 PT)
    beyond the algorithm
      spurious events removal (Chao Ma, 2:20 PT)
      elimination algorithm
  A new adaptive criterion

## Slide 9
A three-pronged strategy to address the challenges
  Pre-requisites for on-shore application (Jing Wu, 4:00 PT)
  Stronger ISS internal-multiple-removal algorithm
    within the algorithm
      incorporate dimension of the source (Xinglu Lin, 1:30 PT)
      incorporate radiation pattern of the source (Jinlong Yang, 1:55 PT)
    beyond the algorithm
      spurious events removal (Chao Ma, 2:20 PT)
      elimination algorithm
  A new adaptive criterion

## Slide 10
A three-pronged strategy to address the challenges
  Pre-requisites for on-shore application (Jing Wu, 4:00 PT)
  Stronger ISS internal-multiple-removal algorithm
    within the algorithm
      incorporate dimension of the source (Xinglu Lin, 1:30 PT)
      incorporate radiation pattern of the source (Jinlong Yang, 1:55 PT)
    beyond the algorithm
      spurious events removal (Chao Ma, 2:20 PT)
      elimination algorithm
  A new adaptive criterion

## Slide 11
A three-pronged strategy to address the challenges
  Pre-requisites for on-shore application (Jing Wu, 4:00 PT)
  Stronger ISS internal-multiple-removal algorithm
    within the algorithm
      incorporate dimension of the source (Xinglu Lin, 1:30 PT)
      incorporate radiation pattern of the source (Jinlong Yang, 1:55 PT)
    beyond the algorithm
      spurious events removal (Chao Ma, 2:20 PT)
      elimination algorithm
  A new adaptive criterion

## Slide 12
A three-pronged strategy to address the challenges
  Pre-requisites for on-shore application (Jing Wu, 4:00 PT)
  Stronger ISS internal-multiple-removal algorithm
    within the algorithm
      incorporate dimension of the source (Xinglu Lin, 1:30 PT)
      incorporate radiation pattern of the source (Jinlong Yang, 1:55 PT)
    beyond the algorithm
      spurious events removal (Chao Ma, 2:20 PT)
      elimination algorithm
  A new adaptive criterion

## Slide 13
Early ideas
Ramírez(2005)
ISS internal multiple elimination

## Slide 14
Early ideas
Ramírez(2005)
Elimination of first order internal multiples generated at the shallowest reflector (1D normal incidence)
Herrera(2012)
ISS internal multiple elimination

## Slide 15
Early ideas
Ramírez(2005)
Elimination of first order internal multiples generated at the shallowest reflector (1D normal incidence)
Herrera(2012)
An internal-multiple elimination algorithm
for all first-order internal multiples for a 1D earth
(This presentation)
ISS internal multiple elimination

## Slide 16
From ISS internal multiple attenuation to elimination
Extra transmission coefficients (attenuation factor)
Why the ISS internal multiple attenuation algorithm predicts approximate amplitude not exactly accurate amplitude?
The structure of this presentation

## Slide 17
From ISS internal multiple attenuation to elimination
Extra transmission coefficients (attenuation factor)
Why the ISS internal multiple attenuation algorithm predicts approximate amplitude not exactly accurate amplitude?
The structure of this presentation

## Slide 18
ISS internal multiple attenuation algorithm
(1D normal incidence version)
Notes: I will show how we get b1 from data later in an example.

## Slide 19
The reflection data is:
δ(t-z/c)
reflector 1
reflector 2
R1
R2
T01
T10
ISS internal multiple attenuation algorithm

## Slide 20
Make a water speed migration of D(t) :
The reflection data is:
δ(t-z/c)
reflector 1
reflector 2
R1
R2
T01
T10
ISS internal multiple attenuation algorithm

## Slide 21
The actual first order internal multiple is:
ISS internal multiple attenuation algorithm

## Slide 22
The ISS attenuation algorithm prediction is:
The actual first order internal multiple is:
ISS internal multiple attenuation algorithm

## Slide 23
The ISS attenuation algorithm prediction is:
The actual first order internal multiple is:
ISS internal multiple attenuation algorithm

## Slide 24
The ISS attenuation algorithm prediction is:
The actual first order internal multiple is:
ISS internal multiple attenuation algorithm

## Slide 25
The ISS attenuation algorithm prediction is:
The actual first order internal multiple is:
ISS internal multiple attenuation algorithm
The time prediction is precise, and the amplitude of the prediction has extra transmission coefficients (attenuation factor) T01T10, which was first discovered and studied in Weglein and Matson (1998)

## Slide 26
A generalization of the attenuation factor:
AFj is the attenuation factor for first order internal multiples with a downward reflection at the jth reflector.

## Slide 27
internal multiples and free-surface multiples
Free-surface
A reflector
A internal multiple
A free-surface multiple

## Slide 28
internal multiples and free-surface multiples
Free-surface
A reflector
A internal multiple
A free-surface multiple
We know

## Slide 29
internal multiples and free-surface multiples
Free-surface
A reflector
A internal multiple
A free-surface multiple
We know
We do not know

## Slide 30
From ISS internal multiple attenuation to elimination
Extra transmission coefficients (attenuation factor)
Why the ISS internal multiple attenuation algorithm predicts approximate amplitude not exactly accurate amplitude?
The structure of this presentation

## Slide 31: For different multiples the attenuation factors are different

## Slide 32
500m
1700m
2700m
5700m
V=1500m/s ρ=1.0g/cm3
V=1700m/s ρ=1.8g/cm3
V=1700m/s ρ=1.0g/cm3
V=3500m/s ρ=4.0g/cm3
V=5000m/s ρ=4.0g/cm3
For different multiples the attenuation factors are different

## Slide 33
P1
P2
P3
M1
M2
For different multiples the attenuation factors are different
P4

## Slide 34
P1
P2
P3
M1
M2
For different multiples the attenuation factors are different
P4

## Slide 35
P1
P2
P3
M1
M2
M1
M2
AF2=(T212T221)T10T01
AF1=T10T01
For different multiples the attenuation factors are different
P4

## Slide 36
M1
M2
For different multiples the attenuation factors are different

## Slide 37: The attenuation factors are related to the second integral

## Slide 38
sub-events into ISS attenuator actual internal multiple
attenuation
factor
sub-events into ISS attenuator actual internal multiple
Extra transmission
coefficients
extra transmission coefficients (attenuation factor)
Notes: It is 1D normal incidence. ………………
The algorithm is fully data driven. Here we show how it works inside the algorithm, we do not separate them in the data.

## Slide 39
From ISS internal multiple attenuation to elimination
Extra transmission coefficients (attenuation factor)
Why the ISS internal multiple attenuation algorithm predicts approximate amplitude not exactly accurate amplitude?
The structure of this presentation

## Slide 40
ISS internal multiple elimination
ISS internal multiple attenuation
ISS internal multiple elimination

## Slide 41
AF
F[b1]
T
R
b1 (data)
Coupled terms
of R and R’
b1(data)
g
ISS internal multiple elimination
b1(data)

## Slide 42
AF
F[b1]
T
R
b1 (data)
Coupled terms
of R and R’
b1(data)
g
ISS internal multiple elimination
b1(data)

## Slide 43
b1(data)
F[b1]
AF
F[b1]
T
R
b1 (data)
Coupled terms
of R and R’
b1(data)
g
ISS internal multiple elimination
b1(data)

## Slide 44
predict internal multiples with correct time and amplitude
Input: data
Flow chart of the ISS internal multiple elimination algorithm

## Slide 45
predict internal multiples with correct time and amplitude
Input: data
Flow chart of the ISS internal multiple elimination algorithm

## Slide 46
predict internal multiples with correct time and amplitude
Input: data
Flow chart of the ISS internal multiple elimination algorithm

## Slide 47
predict internal multiples with correct time and amplitude
Input: data
Flow chart of the ISS internal multiple elimination algorithm

## Slide 48
predict internal multiples with correct time and amplitude
Input: data
Flow chart of the ISS internal multiple elimination algorithm

## Slide 49
predict internal multiples with correct time and amplitude
Input: data
Flow chart of the ISS internal multiple elimination algorithm

## Slide 50: Numerical test for elastic PP data in a 1D earth

## Slide 51
Layer 1: ρ=1.0g/cm3, vp=1500m/s, vs=400m/s
Layer 2: ρ=3.0g/cm3, vp=2000m/s, vs=1200m/s
Layer 4: ρ=1.5g/cm3, vp=1500m/s, vs=1500m/s
Layer 5: ρ=1.8g/cm3, vp=2500m/s, vs=1500m/s
Z1=0m
Z2=300m
Z3=800m
Z4=1900m
Z5=2100m
Z6=2400m
-2500m
0
2500m
12.5m
Layer 3: ρ=2.1g/cm3, vp=1500m/s, vs=900m/s
Yanglei Zou et al. (2014)
Courtesy of Schlumberger De-multiples Team
Internal multiple elimination in an elastic earth
Model

## Slide 52
Yanglei Zou et al. (2014)
Data

## Slide 53
P primaries
Yanglei Zou et al. (2014)
Data
(with arrows pointed to P primaries)

## Slide 54
Converted primaries
Yanglei Zou et al. (2014)
Data
(with arrows pointed to converted primaries)

## Slide 55
P multiples
Yanglei Zou et al. (2014)
Data
(with arrows pointed to P multiples)

## Slide 56
Yanglei Zou et al. (2014)
Data

## Slide 57
A section of the synthetic data where a primary interferes with two internal multiples

## Slide 58
A section of the synthetic data where a primary interferes with two internal multiples
arrow point to a internal multiple
internal multiple

## Slide 59
A section of the synthetic data where a primary interferes with two internal multiples
arrow point to another internal multiple
internal multiple

## Slide 60
A section of the synthetic data where a primary interferes with two internal multiples
arrow point to a primary
converted wave
primary

## Slide 61
A section of the synthetic data after
internal multiple elimination
converted wave
primary

## Slide 62
A section of the synthetic data
with only primaries
converted wave
primary

## Slide 63
The ISS free-surface multiple elimination algorithm and ISS internal-multiple attenuation algorithm are the most capable algorithms today for multiples removal. They are the only methods that do not require any subsurface information to remove multiples.
When the primaries and internal multiples are separated, the ISS internal-multiple attenuation algorithm is adequate to remove all internal multiples. When the primaries and internal multiples are proximal or interfering with each other, the ISS internal-multiple attenuation algorithm is less effective and the new elimination algorithm provides a more effective way to remove the multiples.
The new internal multiple elimination algorithm can eliminate all first-order internal multiples for a 1D earth without knowing any subsurface information. The numerical test for a 1D pre-stack elastic PP data shows very encouraging results.
We are developing an elimination algorithm for 2D and 3D earth by identifying terms in the inverse scattering series.
Summary